## Slide 1: Audio playback using DMA
By:
Kumar sai reddy guntaka

## Slide 2: Features Used
4 user switches | X | 
4 user LEDs | X | 
5 user push buttons |  | X
USB-UART Bridge |  | X
Micro SD card connector | X | 
HDMI Sink and HDMI Source | X | 
16 Bit VGA port | X | 
Audio codec w/ three 3.5mm jacks |  | X
User EEPROM | X | 
10/100/1000 Ethernet PHY | X | 
512MiB 800Mt/s DDR3 Memory |  | X
Serial Flash | X | 
Five Pmod ports | X | 
Pmod for XADC signals | X | 
USB HID Host | X | 
Not used | used

## Slide 3: Audio:
An Analog Devices SSM2603 Audio Codec provides integrated digital audio processing to the Zynq-7000 AP SoC. It allows for stereo record and playback at sample rates from 8 kHz to 96 kHz.
On the analog side, the codec connects to three 3.5 mm standard audio jacks. There are two inputs: a mono microphone and a stereo line in. There is one stereo output, the headphone jack. Analog power is provided by a dedicated linear power supply (IC5).

## Slide 4: Sampling Rate:
Sampling rate or sampling frequency defines the number of samples per second (or per another unit) taken from a continuous signal to make a discrete or digital signal.
fs = 1/T.
f Nyqu = 2 f i n , max.
In audio production, a sample rate (or "sampling rate") defines how many times per second a sound is sampled. Technically speaking, it is the frequency of samples used in a digital recording.

## Slide 5: Protocols:
The digital interface of the SSM2603 is wired to the programmable logic side of the Zynq. Audio data is transferred via the I²S protocol. Configuration is done over an I2C bus. The device address of the SSM2603 is 0011010b. All digital I/O are 3.3V level and connect to a 3.3V-powered FPGA bank.

## Slide 6: Implementing I2S protocol:
I²S (Inter-IC Sound, is an electrical serial bus interface standard used for connecting digital audio devices together. It is used to communicate PCM audio data between integrated circuits in an electronic device. The I²S bus separates clock and serial data signals, resulting in simpler receivers than those required for asynchronous communications systems that need to recover the clock from the data stream

## Slide 7: I2C Communication Protocol:
I2C stands for Inter-Integrated Circuit. It is a bus interface connection protocol incorporated into devices for serial communication. It was originally designed by Philips Semiconductor in 1982. Recently, it is a widely used protocol for short-distance communication. It is also known as Two Wired Interface(TWI).

## Slide 8: Vivado:
Hardware implementation:
Add IP’s.
Configure the blocks.
Validate the design.
Create the HDL wrapper.
Generate bitstream.
And export the hardware.

## Slide 9: Let's discuss about few IP’s used in project and their configuration.

## Slide 10: Source Code:

## Slide 11: Software Implementation:
Open Xilinx SDK and add the source files that which we discussed.
Build the project
Program the device.
Add port in SDK terminal where you can see the instructions.
Button | Function
BTN0 | no effect
BTN1 | record from mic in
BTN2 | play on hph out
BTN3 | record from line in

## Slide 12: Demo:
https://drive.google.com/file/d/1eyTRJqBjKK-WUUt6TKoq4aMENxMIuqsf/view?usp=sharing

## Slide 13
Thank you